## Slide 1: FYP DEMO Machine Learning and Data Fusion For An Intelligent Wearable Device
Galada Aditya
U1422406K

## Slide 2: Outline
1. ECG R Peak Detection
2. ECG Signal Processing and Analysis
3. Respiratory Rate Estimation
4. Adaptive Filtering of ECG
5. Bio Signal Based Age Classification
6. Heart Sound Anomaly Classification

## Slide 3: ECG R Peak Detection
1. R Peak Detection
ECG – electrical voltage produced by cardiac muscle contraction and expansion.
R peaks – reference marker for each cycle
Accurate detection important – rhythm analysis
3. Proposed MEE Scheme
4. Results
2. Pan Tompkins Algorithm
 | Acc – MEE | Acc - PT | Improvement
1 | 99.479 | 99.577 | 0.098
2 | 90.700 | 97.686 | 6.986
3 | 90.647 | 96.093 | 5.446
4 | 88.178 | 91.264 | 3.086
5 | 91.538 | 96.049 | 4.511
6 | 98.843 | 98.442 | -0.402
7 | 98.346 | 99.322 | 0.976
8 | 83.336 | 84.911 | 1.576
9 | 94.031 | 95.970 | 1.940
10 | 99.509 | 99.111 | -0.398
11 | 94.970 | 96.379 | 1.409
12 | 97.398 | 97.368 | -0.030
TOTAL | 93.950 | 95.979 | 2.028
Overall improvement in accuracy
FP beats reduce : 3122 for PT , 1447 for MEE.
Acc. improve by 6.9% for patient 2, noisy signal.
MEE criterion aims to minimize the entropy of error between measured and desired signal
Initial reference signal - averaging the QRS complexes detected by PT method.
Measured input signal - windowed noisy ECG.
The QRS complex is slid across the ECG signal and the cost function at each step is recorded and the reference signal is regularly updated.
Peaks in this plot correspond to ECG R peaks.
Traditionally used method – PT algorithm
Filtering – Differentiation – Squaring – Integration
Susceptible to muscle and motion noise

## Slide 4: ECG Signal Processing and Analysis
1. Cardiac Rehab
Data collected from 12 patients undergoing cardiac rehabilitation exercises.
Prescribed 3 exercises – TM SC AC/IR
Program Structure
Warmup : Ex1 : Rest : Ex2 : Rest : Ex3 : Cool down
2 Methods of data collection
Intermittent physiological monitor
Wearable device with ECG sensors
2. Conventional Monitors
3. ECG Monitoring Results
3. ECG Monitoring Results – Cont’d
No | Target HR (bpm) | TM | SC | AC/IR | AC/IR | Pre-rehab | Post-rehab
 |  | Exercise HR (bpm) |  |  |  | Blood Pressure(mm Hg) HR (bpm) | 
1 | 90~100 | 94 | 96 |  | 103 | 114/64, 71 | 107/65, 76
2 | 100~105 | 94 | 98 |  | 104 | 120/59, 60 | 108/50, 62
3 | 85~90 | 84 | 89 |  | 82 | 117/61, 62 | 103/58, 74
4 | 100~110 | 105 | 111 |  | 95 | 131/81, 68 | 104/68, 87
5 | 90~95 | 72 | 82 |  | 83 | 153/75, 56 | 113/60, 60
6 | 95~100 | 117 | 105 |  | 86 | 133/86, 65 | 123/73, 73
7 | 102~110 | 90 | 103 |  | 113 | 148/66, 72 | 123/67, 76
8 | 80~85 | 107 | 105 |  | 95 | 102/65, 77 | 103/58, 79
9 | 70~80 | 77 | 74 |  | 66 | 126/60, 56 | 122/68, 58
10 | 85~90 | 100 | 87 |  | 85 | 137/70, 66 | 135/65, 70
11 | 110 | N.A. | 105 |  | 94 | 149/65, 61 | 138/64, 94
12 | 100 | 105 | 92 |  | 87 | 152/89, 70 | 138/60, 78
Blood pressure decreased and heart rate increased after rehab
Target heart rate was met – in general
Limitation – single point readings
R Peak detection performed
Inter-beat interval calculated
Plot of heart rate vs time obtained
Closely reflects the exercise regimen
More detailed and continuous information
Exercise wise analysis
Patient 1,7 assigned IR have higher mean HR and lower sdHR than other exercises. => is intensive and requires a consistent effort.
8/10 patients assigned AC have lower HR than other exercises. => intensity of this exercise is relatively lower.
ECG monitoring adds value to rehab exercise.
Publication : Aditya Galada, Jianmin Zhang, Yong Kiang Yeo, Wee Ser, Zhiping Lin, Doris Tan, Yvonne Chow, Swapna Tony, Jaclyn Chow and David Foo, “ECG Signal Processing and Analysis for Data Arising from Rehab Patients Doing Exercises,” IEEE ISCAS 2018, Florence, Italy, May, 2018, accepted.

## Slide 5: Respiratory Rate Estimation
1. RSA
Respiratory rate – important vital sign
Direct respiration rate measurement – difficult
Possible to derive respiration from ECG
Heartbeat intervals increase during inhalation, decrease during exhalation
3. Autoregressive model
4. Instantaneous Frequency Tracking
2. Power Spectrum
6. Result
Refer to plots in MATLAB GUI
Window the ECG signal into 1 minute sections
Shift of 10 seconds between successive windows
Obtain power spectrum plot of ibi
Peak power -> respiratory frequency
Window the ECG signal into 30 minute sections
Shift of 5 seconds between successive windows
Generate the autoregressive model of ibi series
Dominant pole -> respiratory frequency
Limitations of PSD and AR
- Use window, do not give instantaneous values
- Cannot track the RR rate closely
Instantaneous Frequency Tracking
Use of an adaptive filter.
Weights of IIR bandpass filter recursively updated.

## Slide 6: Adaptive Filtering of ECG Signal
1. Noise Cancellation Setup
2. Noise Simulation
4. Result
Input SNR dB | MEE Improvement dB | LMS Improvement dB
-6 | 24.9303 | 19.9502
-3 | 22.7115 | 19.2311
0 | 20.2217 | 18.3487
3 | 17.5369 | 17.4543
6 | 14.7202 | 16.5423
Input SNR dB | MEE Improvement dB | LMS Improvement dB
-6 | 24.9303 | 19.9502
-3 | 22.7115 | 19.2311
0 | 20.2217 | 18.3487
3 | 17.5369 | 17.4543
6 | 14.7202 | 16.5423
Input SNR | MEE Improvement | LMS Improvement
-6 | 19.7953 | 19.0408
-3 | 18.6016 | 17.9184
0 | 17.3917 | 16.7865
3 | 15.9326 | 15.6144
6 | 14.3588 | 14.4536
Baseline Wander Removal
Electrode Motion Artifact Removal
Muscle Noise Removal
3 types of noise obtained from MIT – NSTDB
Experiments performed using MEE and LMS algorithms at SNR [-6 -3 0 3 6] dB
MEE found to outperform in cases of poor signal quality (low SNR)
Adaptive filtering for noise cancellation
Primary Signal – noise contaminated ECG
Reference Signal – corelated only with noise
Possible to adaptively model the noise in ECG and cancel it with help of a secondary reference.
Try two algorithms – Minimum Error Entropy and Least Mean Square

## Slide 7: Bio Signal Based Age Classification
1. Pre-processing
Use of ECG and Resp. signal for age prediction
Data obtained for 40 patients from Fantasia Database. 20 young, 20 old
Pre-processing – use of FIR bandpass filters
2. Feature Extraction
5. Data Fusion Scheme
Extraction of HRV features from ECG Signal
Motive – known that HRV decreases with age
3. Classification Model - SVM
4. Classification Model - KNN
Class 1
Class 2
K=1
K=3
New Example
?
Distance
Training Instance
6. Result
Refer to plots in MATLAB GUI

## Slide 8: Heart Sound Anomaly Classification
1. Input Signal
2. Feature Extraction
4. Results
Total of 18 features extracted :
Linear Predictive Coefficients
Entropy Based Features
Wavelet Transform
Power Spectrum Features
Mel Frequency Cepstral Coefficients
3. Ensemble of Neural Network
 | PCG Feature Based Classifier |  |  | ECG Feature Based Classifier |  |  | Data Fusion |  | 
 | Se % | Sp % | Acc % | Se % | Sp % | Acc % | Se % | Sp % | Acc %
Mean | 76.094 | 87.112 | 83.250 | 79.812 | 86.803 | 85.000 | 75.855 | 93.732 | 88.750
SD | 13.131 | 5.058 | 6.329 | 16.764 | 6.658 | 5.244 | 16.831 | 2.054 | 6.149